# Description

Wireless LAN uses radio frequencies to transmit and receive data between PC’s or other network devices without wires or cables. The applications of wireless LAN include independent networks (suitable for small or temporary peer-to-peer configurations) and infrastructure networks, offering fully distributed data connectivity via micro cells and roaming.

The TWL-C11A Wireless LAN PC Card is designed and manufactured by Tellus Group Corporation --- a company with expertise in wireless communication sector. Its performance and reliability exceed the requirements of IEEE 802.11b standard, and its interoperability and plug-and-play features make installation quite easy.

# Features

- Automatic data rate fallback under noisy environment

- Advanced power management for battery saving

- Supports a wide range of operating systems

- Interoperable with IEEE 802.11b compliant equipment

- Supports full mobility and seamless roaming from cell to cell

- Plug-and-play installation and easy client management with utility software

- Up to 300m operating range (environment dependent)

# Applications

  - Home networking for device sharing

  - Frequently changing or hard-to-wire environments

  - SOHO (Small Office and Home Office) users

- Inter-building connection

# Specifications

    - General:

      - Compliant with IEEE 802.11b standard

      - Security: WEP 128 bit, encryption MD5

- Hardware

      - RF Range: 2.4 ~ 2.4835 GHz

      - Data rate: 11 / 5.5 / 2 / 1 Mbps

      - Modulation:
DSSS (Direct Sequence Spread Spectrum)

DBPSK/DQPSK

      - Coding: 
11 chip/bit Barker Coding for 1 / 2 Mbps
Complementary Code Keying for 5.5 / 11 Mbps

      - Number of channels:
Europe: 13 (3 non-overlapping)
US: 11 (3 non-overlapping)
France: 4 (1 non-overlapping)
Japan: 14 (3 non-overlapping)

      - Host interface:
PC Card 95
PCMCIA type II 16 bit

      - Transmit power (Typ.): +15 dBm

      - Receive sensitivity (Typ.): 
-83 dBm for 11Mbps; -88 dBm for 5.5 / 2 / 1 Mbps (@BER 10E-5)

      - Current Drain (max. @3.3 V): Tx mode: 320 mA; Rx mode: 190 mA; standby mode: 30mA

- Software

  - Driver support: 
Windows 95 / 98 / 2000 / ME / CE / NT, Linux

  - Utility: User setup & diagnostics tool

- Mechanical

  - One integrated patch antenna, and one Sx-type connector for external antenna

  - Green LED for activity Indication

  - Input Voltage: 3.3V

  - Environmental:
0 ~ +55°C operating temperature
Humidity 95% (non-condensing)

  - Package: PCMCIA type II extended

  - Dimensions: 116.2 x 54.0 x 7.0 mm

  - Weight: Less than 50 grams

  - EMC Certificate

U.S., Canada: FCC Part 15, sections 15.247, 15.205, 15.209; RSS-210

Europe: ETS 300 328, ETS 300 826, CE Marked

Japan: RCR STD-33

Notes: 1. TWL-PCA Adapter is available as an option for the wireless networking of desktop PCs.

2. PC Card with two built-in PCB patch diversity antennas is also available.

3. Specifications subject to change without notice.

Tellus Group Corporation

4F, No.15, Industry E. Rd. IX, Science-Based Industrial Park, Hsinchu, Taiwan, R.O.C.

Tel: +886 3 5780275           Fax: +886 3 5780279

E-mail: sales@tellus.com.tw    http://www.tellus.com.tw

# Text boxes

ISO9001: 2000 certified